## Slide 1: Managing DRAM Latency Divergence in Irregular GPGPU Applications
Niladrish Chatterjee
Mike O’Connor
Gabriel H. Loh
Nuwan Jayasena
Rajeev Balasubramonian

## Slide 2: Irregular GPGPU Applications
Conventional GPGPU workloads access vector or matrix-based data structures
  Predictable strides, large data parallelism
Emerging Irregular Workloads
  Pointer-based data-structures & data-dependent memory accesses
  Memory Latency Divergence on SIMT platforms
  Warp-aware memory scheduling to reduce DRAM latency divergence

## Slide 3: SIMT Execution Overview
GDDR5
Channel
L1
Warp 1
Warp Scheduler
SIMD Lanes
Memory Port
Warp 2
Warp 3
Warp N
SIMT Core
SIMT Core
SIMT Core
I
N
T
E
R
C
O
N
N
E
C
T
L2 Slice
Memory Controller
GDDR5
Channel
Memory Partition
THREADS
Memory Partition
Warps
GDDR5
GDDR5
L2 Slice
Memory Controller
Lockstep execution
Warp stalled on memory access

## Slide 4: Memory Latency Divergence
Coalescer has limited efficacy in irregular workloads
Partial hits in L1 and L2
  1st source of latency divergence
DRAM requests can have varied latencies
  Warp stalled for last request
DRAM Latency Divergence
Load Inst
SIMD Lanes (32)
Access Coalescing Unit
L1
L2
GDDR5

## Slide 5: GPU Memory Controller (GMC)
Optimized for high throughput
Harvest channel and bank parallelism
  Address mapping to spread cache-lines across channels and banks.
Achieve high row-buffer hit rate
  Deep queuing
  Aggressive reordering of requests for row-hit batching
Not cognizant of the need to service requests from a warp together
  Interleave requests from different warps leading to latency divergence

## Slide 6: Warp-Aware Scheduling
SM 1
SM 2
A: LD
A
A
A
A
B
B
B
B
MC
A: Use
Baseline
GMC Scheduling
A
B
A
A
A
B: Use
B
B
B
Stall Cycles
Stall Cycles
Warp-Aware Scheduling
A
A
A
B
B
A
B
B
A: Use
Stall Cycles
B: LD
Reduced Average Memory Stall Time

## Slide 7: Impact of DRAM Latency Divergence
If all requests from a warp were to be returned in perfect sequence from the DRAM –
~40% improvement.
If there was only 1 request per warp – 5X improvement.

## Slide 8: Key Idea
Form batches of requests from each warp
  warp-group
Schedule all requests from a warp-group together
Scheduling algorithm arbitrates between warp-groups to minimize average stall-time of warps

## Slide 9: Controller Design

## Slide 10: Controller Design

## Slide 11: Warp-Group Scheduling : Single Channel
Pending Warp-Groups
Warp-group priority table
Transaction Scheduler
# of reqs in warp-group
Row hit/miss status of reqs
Queuing delay in cmd queues
Pick warp-group with lowest runtime
Each Warp-Group assigned a priority
  Reflects completion time of last request
Higher Priority to
  Few requests
  High spatial locality
  Lightly loaded banks
Priorities updated dynamically
Transaction Scheduler picks warp-group with lowest run-time
  Shortest-job-first based on actual service time

## Slide 12: WG-scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG

## Slide 13: Multiple Memory Controllers
Channel level parallelism
  Warp’s requests sent to multiple memory channels
  Independent scheduling at each controller
Subset of warp’s requests can be delayed at one or few memory controllers
Coordinate scheduling between controllers
  Prioritize warp-group that has already been serviced at other controllers
  Coordination message broadcast to other controllers on completion of a warp-group.

## Slide 14: Warp-Group Scheduling : Multi-Channel
Pending Warp-Groups
Priority Table
Transaction Scheduler
# of reqs in warp-group
Row hit/miss status of reqs
Queuing delay in cmd queues
Pick warp-group with lowest runtime
Status of Warp-group in other channels
Periodic messages to other channels about completed warp-groups

## Slide 15: WG-M Scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG
WG-M

## Slide 16: Bandwidth-Aware Warp-Group Scheduling
Warp-group scheduling negatively affects bandwidth utilization
  Reduced row-hit rate
Conflicting objectives
  Issue row-miss request from current warp-group
  Issue row-hit requests to maintain bus utilization
Activate and Precharge idle cycles
  Hidden by row-hits in other banks
Delay row-miss request to find the right slot

## Slide 17: Bandwidth-Aware Warp-Group Scheduling
The minimum number of row-hits needed in other banks to overlap (tRTP+tRP+tRCD)
  Determined by GDDR timing parameters
  Minimum efficient row burst (MERB)
Stored in a ROM looked up by Transaction Scheduler
More banks with pending row-hits
  smaller MERB
Schedule row-miss after MERB row-hits have been issued to bank

## Slide 18: WG-Bw Scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG
WG-M
WG-Bw

## Slide 19: Warp-Aware Write Draining
Writes drained in batches
  starts at High_Watermark
Can stall small warp-groups
When WQ reaches a threshold (lower than High_Watermark)
  Drain singleton warp-groups only
Reduce write-induced latency

## Slide 20: WG-scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG
WG-M
WG-Bw
WG-W

## Slide 21: Methodology
GPGPUSim v3.1 : Cycle Accurate GPGPU simulator
USIMM v1.3 : Cycle Accurate DRAM Simulator
  modified to model GMC-baseline & GDDR5 timings
Irregular and Regular workloads from Parboil, Rodinia, Lonestar, and MARS.
SM Cores | 30
Max Threads/Core | 1024
Warp Size | 32 Threads/warp
L1 / L2 | 32KB / 128 KB
DRAM | 6Gbps GDDR5
DRAM Channels Banks | 6 Channels 16 Banks/channel

## Slide 22: Performance Improvement
Chart: IPC Normalized to Baseline
| WG | WG-M | WG-Bw | WG-W
Column1 | 0.034 | 0.062 | 0.084 | 0.101
Reduced Latency Divergence
Restored Bandwidth Utilization

## Slide 23: Impact on Regular Workloads
Effective coalescing
High spatial locality in warp-group
WG scheduling works similar to GMC-baseline
  No performance loss
WG-Bw and WG-W provide
  Minor benefits

## Slide 24: Energy Impact of Reduced Row Hit-Rate
Scheduling Row-misses over Row-hits
  Reduces the row-buffer hit rate 16%
In GDDR5, power consumption dominated by I/O.
Increase in DRAM power negligible compared to execution speed-up
  Net improvement in system energy
Chart: GDDR5 Energy/bit
| Baseline | WG-Bw
I/O | 18.1 | 18.1
Row | 8.4151 | 9.7615
Column | 6.21 | 6.21
Control | 0.31 | 0.31
DLL | 0.44 | 0.44
Background | 0.88 | 0.88

## Slide 25: Conclusions
Irregular applications place new demands on the GPU’s memory system
Memory scheduling can alleviate the issues caused by latency divergence
Carefully orchestrating the scheduling of commands can help regain the bandwidth lost by warp-aware scheduling
Future techniques must also include the cache-hierarchy in reducing latency divergence

## Slide 26: Thanks !

## Slide 27: Backup Slides

## Slide 28: Performance Improvement : IPC

## Slide 29: Average Warp Stall Latency

## Slide 30: DRAM Latency Divergence

## Slide 31: Bandwidth Utilization

## Slide 32: Memory Controller Microarchitecture

## Slide 33: Warp-Group Scheduling
Every batch assigned a priority-score
  completion time of the longest request
Higher priority to warp groups with
  Few requests
  High spatial locality
  Lightly loaded banks
Priorities updated after each warp-group scheduling
Warp-group with lowest service time selected
  Shortest-job-first based on actual service time, not number of requests